## Slide 1: PHoEnix Association presents VERILOG WORKSHOP
Day 1
Overview of Digital design and circuits

## Slide 2: Some identities of Boolean Algebra
x+0=x
x+x’=1
x+y=y+x
x.1=x
x.x’=0
x+x=x
(x’)’=x
x+xy=x
x.x=x
x(x+y)=x
De-Morgan’s Law:
(x+y)’=x’.y’
(x.y)’=x’+y’

## Slide 3: Algebraic Simplification of Boolean Functions
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
F= A’BC’ + AB’C’ + AB’C + ABC’ + ABC
F= A’BC’ + AB’(C’ + C) + AB(C’ + C)
F= A’BC’ + A(B’ + B)
F= A’BC’ + A
F= A’BC’ + A + ABC’ since x+xy=x
F= (A’ + A)BC’ + A
F=A+ BC’
Each of these is called a minterm
F
Represented as SOP
SOP= Sum of Products

## Slide 4: K-Maps: A better way of simplification
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
A
BC
00 01 11 10
0
1
Some points about K-maps:
A K-map made up of squares, each square represents a minterm /maxterm
Number of squares depend on number of input combinations
Only one bit variation between adjacent squares
1
1
1
1
1
F= A + BC’

## Slide 5: Design of Digital circuits
There are 2 types of circuits: Combinational and sequential
Combinational circuits: A Combinational logic circuit consists of a set of logic gates whose outputs at any time are determined from only the present combination of inputs
Sequential Circuits: A sequential logic circuit consists of a set of logic gates whose outputs at any time are determined from the present combination of inputs as well as previous output

## Slide 6: 7-Segment Display Coder

## Slide 7: Half Adder

## Slide 8: Full Adder
B Cin
A
00 01 11 10
0
1
A
B Cin
0
1
00 01 11 10
For S
For Cout
S = A + B + Cin
Co= AB + Ci(A + B)
1
1
1
1
1
1
1
1
Chessboard configuration => XOR function

## Slide 10: Half Subtractor
Half Subtractor
x y
D B
A | B
0 | 0
0 | 1
1 | 0
1 | 1
D | Bo
0 | 0
1 | 1
1 | 0
0 | 0
D= A + B
Bo= A’B

## Slide 11: Full Subtractor

## Slide 12: 2-Bit Multiplier
B1 B0
A1 A0
B1A0 B0A0 B0A1
C3 C2 C1 C0
X
B1A1

## Slide 13: Multiplexers
It is a combinational circuit that selects binary information from one of the many input lines and directs it to the output line.
1
0
S
I0
I1
O/P
m=log n
2
No. of i/p lines
No. of select lines

## Slide 14: 2:1 MUX
1
0
S
I0
I1
O/P
S | I0 | I1 | O/p
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
S | O/P
0 | I0
1 | I1
Simplified truth table
o/p = I0.S’ + I1. S

## Slide 15: 4:1 MUX
1
0
I0
I
1
O/P
3
2
I2
I3
S0
S1
O/P = S1’S0’I0 + S1’S0I1 + S1S0’I2 + S1S0I3

## Slide 16: MUX Tree
3 2:1 MUX required to implement a 4:1 MUX
4/2 = 2 2/2 =1
2+1= 3 2x1 MUX required
S1
S0

## Slide 17: 8X1 MUX using 4X1 MUX
E
E
=> 2.5 4X1 MUX required

## Slide 18: Demultiplexers
One input, multiple outputs
Reverse operation of MUX
Called data distributor
m=log n
2
No. of o/p lines

## Slide 19: 1:2 Demux

## Slide 20: 1:4 Demux

## Slide 21: Encoders

## Slide 22: Encoders

## Slide 23: Encoders

## Slide 24: Decoders

## Slide 25: Decoders

## Slide 26: Decoders

## Slide 27: Decoders